"DOORS"
a local, centralized control system
for a set of automatic doors

1. Introduction

The "Doors" system aims to elegantly fulfill a set of requirements common to most apartment buildings and many other facilities: management and monitoring of multiple physical entry-points,
and serving of common "intercom" features to an arbitrary number of "client" or "apartment" units,
all coordinated through a central hub unit.

2. The Door Unit

The Door Unit consists of:
- an STM32 Nucleo-F756ZG board;
- a servo-motor controlling an automatic door;
- an LCD touch display for passcode entry & "bell" functions;
- a safety sensor, to detect blockage and avoid unfortunate accidents;
- a small QVGA camera, mainly for Intercom functions;
- an additional power supply unit, to supplement the one on the board.

Each Door shares an I2C bus with the Hub and all other Door units, and participates in the bus passively as an I2C Target.

3. The Intercom Unit

The Intercom Unit consists of:
- an ESP32 WROOM-32 board;
- an LCD touch display for door information & control;
- a speaker for the "bell" function.

Each Intercom is connected to a local network, and functions as a client with the singular Hub unit as its server.
Internally, the Intercom is a simple FreeRTOS based system, with its two primary tasks being handling the touch display and Hub communications.

4. The Hub Unit

The Hub Unit consists of a single Beaglebone Green board.

The Hub is physically connected to an I2C bus it shares with all Door units, and functions as the one and only I2C Controller of this bus. Some additional hardware, not covered here, is likely necessary for this bus to function over application-useful distances.
The Hub is also connected to a local network, where it functions as a server, with all local Intercom units as its clients.

Internally, the Hub is a Debian Linux system continuously running multiple processes:
- "Door Manager", handling I2C communication with the Door units;
- "Intercom Server", handling socket communication with the Intercom units;
- "Event Database Service", wrapping a local Sqlite database for access by other processes.